## Slide 1: Implementing 802.11ah
Migration analysis from a 802.11/a/g/p transceiver in GNUradio
D. Zwart Technical University of Delft
Delivered: 16-05-2018

## Slide 2: Pre-word
Documentation associated with this presentation can be found in wiki. Please refer to this github wiki for updated references to:
  Reports
  Papers
  Matlab sources
  GNUradio sources
Slides show a (->) link in the title, which links to the wiki.
TX: transmitter end (simple)
RX: receiver end (complex  equalization)

## Slide 3: Contents
Previous developments
  Achievements D. Verhaert
  Limitations (changes to make model work)
Current work
  Goals w.r.t reality
  + Achievements
  + Documentation
Points of attention
Future implementation

## Slide 4: Previous developments (1/2) (->)
Goal: GNUradio transceiver with
  USRP N210 SDR with 2x VERT900 antenna’s
  Ubuntu 16.04 LTS
  Pybombs & GNUradio (long prefix build time)
Installation guide by D. Verhaert avoids GNUradio, Apache & USRP driver trouble
Given block model, slightly adapted

## Slide 5: D. Verhaert achievements (->)
GNUradio transceiver with slight adaptations:
  Based on 2.4GHz 802.11a/g/p
    Added USA frequency option (902 – 928 MHz)
    Set channel BW to 2 MHz
    Added file sink as capture (FileSinkah)
    Attempted higher MCS indices, removed because of packet loss.
    Successfully transmitted small WiFi payloads (no ETH layer, pure PHY+MAC)
  Reproducible results

## Slide 6: Previous developments (2/2) (->)
Removed an experimental Correct IQ block (Commit)
Fix GNUradio root access to OOT blocks (Out-Of-Tree) (sudo shell script, TODO link)
Block model was now runnable.
More configuration needed…

## Slide 7: Limitations (1/3)
Very chaotic block scheme, flow connections all over the place.
Malformed packets (Wireshark), or no packets received at all.
USRP buffer overflow
Very spread-out OFDM subcarrier I/Q constellation points.

## Slide 8: Limitations (2/3)
Fixes to GNUradio configurations:
USRP TX “LO offset”
  Set to 6 MHz in order to be able to receive packets (why?)
Sampling rate had to be at least 2 MHz
  Sampling rate == Channel bandwith (I/Q)
  Channel bandwith of 1 MHz didn’t work
  802.11ah proposal demands robustness in STF and LTF.
  Robustness changes not yet implemented.

## Slide 9: Limitations (3/3)
Added European frequency band
  (863 – 868 MHz)
High MCS index -> no reliable reception
  QAM64 didn’t work, didn’t even try QAM256
Intermezzo:
  A lot was lacking in not only the model, but also the underlaying OOT blocks.
  Find literature & understand OFDM concepts first before applying anything in GNUradio or C++.

## Slide 10: Current work (1/15)
Goals
  Implement ‘low hanging fruit’ changes for 802.11ah PHY in model and sub-model blocks.
  Study 802.11ah PHY & MAC layer interaction.
Reality
  Lack of knowledge or new to:
    GNUradio, OFDM, encoding
  Changes have snowball effect due to ‘hardcoded’ or static state of 802.11a/g/p model
  TX side barely adjustable, complexity too high
Approach
  Find lots and lots of reliable / filtered resources
  Document everything
  Implement only top-level changes for clarity

## Slide 11: Current work – goals (2/15)
Specific goals
  Learn about PHY specification
    MCS changes
    S1G vs no-HT / HT / VHT
    Sync changes
    OFDM changes
  Learn about OFDM
    Symbol to carriers (Pilot, data, guard carriers)
    Encoding (interleave, scramble, etc.)
    Cyclic prefixing
  Document changes in code

## Slide 12: Current work – S1G (3/15)
S1G types (mathworks)
  Very similar to 802.11ac!
  Changes are simple on TX side, very complex on RX side.
  Skip RX, do TX only. Adjust goals

## Slide 13: Current work – S1G (4/15)
S1G types (mathworks)
  Beamforming requirements are out of scope
  Repeated PHY fields introduced for following 3 types:
    S1G_1M (1MHz)
      Introduces MCS10, repeated BPSK 1/2, +3dB STF)
      STF, LTF, SIG fields repeated
    S1G_SHORT (>1MHz)
      LTF2 … LTFN introduced
      Most similar to legacy 802.11 PHY
    S1G_LONG (>1MHz)
      SIG-A field
      D-STF
      D-LTF1…N
      SIG-B field
MCS10 vs MCS0 (src)

## Slide 14: Current work – S1G (5/15)
S1G types (mathworks)
  Needs to be added to top level as either:
    Qt dropdown (static)
    Signal generation block (adjustable, dynamic?)
    TX side
      PHY OFDM allocator won’t accept these inputs…
    RX side
      Long Sync, Short Sync & Frame Equalizer need great deal of adjustment (too complex, static, bit-banging?)

## Slide 15: Current work – MCS (6/15) (->)
MCS changes (book-keeping)
  256-QAM (all S1G types)
  BPSK 2x (S1G_1M only)
  TX side:
    Top-level
      Add to QT-GUI dropdown
    WiFi PHY Hier block
      WiFi Mapper block (Mapper)
        OFDM params (Utils)
        Puncturing (Utils)
      Chunks to symbols (.cc, .h)
  RX side
    Sync Short :|
    Sync Long Block :S
    Frame Equalizer :O

## Slide 16: Current work – OFDM (7/15) (->)
802.11ah OFDM carrier mapping (paper, (->))
Same as 802.11ac
Surely the carriers in GNUradio aren’t statically allocated…
BW | FFT bins | Data | Pilot | Carrier distr.
1 MHz | 32 | 24 | 2 | 26 sub, 5 guard, 1 DC
2 MHz | 64 | 52 | 4 | 56 sub, 7 guard, 1 DC
4 MHz | 124 | 108 | 6 | 114 sub, 9 guard, 1 DC
8 MHz | 256 | 234 | 8 | 250 sub, 13 guard, 1 DC
16 MHz | 512 | 468 | 18 | 484 sub, 27 guard, 1 DC

## Slide 17: Current work (8/15) (->)
Oh god… (doxygen)
An Out-Of-Tree block needs to be built called HaLow OFDM Carrier Allocator (doxygen).
Could be accompanied with HaLow Sync Generator (for custom STF, LTF)
Parameters:
  Travelling pilots (boolean)
  Debug (boolean)
  Length tag key (string)
  Bandwidth (int)
Inputs:
  Data stream (pmt)
  Sync words (vector)
Output:
  OFDM symbols
Semantics
  It should throw warnings when data carriers are left unused.
  It should throw exceptions when pilot carriers overlap data carrier indices
  Build function mapping bandwidth to predefined pilot carriers, etc.
BW | FFT | D | P
1 MHz | 32 | 24 | 2
2 MHz | 64 | 52 | 4
4 MHz | 124 | 108 | 6
8 MHz | 256 | 234 | 8
16 MHz | 512 | 468 | 18

## Slide 18: Current work – Block model(9/15)
Is the block model working correctly?
  Yes: for 20 MHz (WiFi)
  No: for 1,2 MHz (HaLow Europe)
Is the model clear?
  Yes: PHY and MAC clearly presented
  No:
    Clutter around it
    PHY layer copied into top-layer?

## Slide 19: Current work – New model (10/15)

## Slide 20: Current work – New model (11/15)
Organized into 3 lab setups:
  Direct loopback (new, no channel!)
    If loopback is broken: the code is broken
  USRP
    If this doesn’t work:
      LO offset = 6 MHz?
      Probably didn’t follow specs correctly
      Wrong antenna? VERT900 vs VERT2400
      Software suitable? (reference)
  File sink / source
    Never used  Wireshark sink is handier
    Can be used for automated unit testing on higher abstraction level?

## Slide 21: Current work – New model (12/15)
  Virtualized so no new routes are needed (just disable/enable blocks)

## Slide 22: Current work – PHY Hier (13/15)
  Transmitter just organized and studied, nothing changed.

## Slide 23: Current work – PHY Hier (14/15)
  Receiver; put correlator blocks into Correlator Hier (`wifi_corr_hier.grc`)
  Added more debugging output
  Organized input vs output better

## Slide 24: Current work – GUI (15/15)
Direct loopback shows clearer results
about bad or good detection.
(For example, when the correlator is
not connected properly, the constellation shows no points,
but the signals do arrive.)
Debugging output

## Slide 25: Points of notice
Although this presentation lacks information about MAC layer:
  AID, RAW, TIM, TXOP, SST, Virtual Carrier Sense, Beamforming (MIMO)
  They were studied
  Infeasible without a structured PHY layer
  Hard to test with 1 USRP

## Slide 26: Future implementation
Skip RX for now, focus on TX.
Start with OFDM block replacement
  Conform S1G specification
Add MCS-8,9,10
Add TX output debugging
Change MAC fields
  (moving QoS, HT to PHY... removing Duration)
Change PHY fields
  (moving QoS, HT to PHY... NDP type MAC content to PHY for VCS in NAV)

## Slide 27: MAC layer (->)
Small changes
  Conditional field sizes (type)!
  Null Data type packet (NDP, out of scope)

## Slide 28: PHY layer (url)
Major changes
  NDP SIG-field adjustment?
  Packet type depency?
vs

## Slide 29: PHY - SIG field
Major changes (IEEE specs)
  Adjusted to fancy features by 802.11ah/ac

## Slide 30: For more info
https://github.com/... Fully documented Wiki