## Slide 1: Revisit 2MHz SIG Field
Date: 2012-03-12
Authors:

## Slide 2
Authors continued:
Slide 2

## Slide 3
Authors continued:

## Slide 4: Abstract
This presentation fixes a bug in the >=2MHz SIG field in current TGah spec framework.

## Slide 5: Background
In TGah, for 4/8/16MHz BWs, the 2MHz SIG is repeated in each 2MHz sub-band
  With some phase shift to reduce PAPR
  Similar to 11ac.
Receiver doesn’t know the BW (2/4/8/16MHz) until decoding the SIG field
  Same as in 11ac, where the receiver may decode SIG field in the primary 2MHz only
  Requires LTF1 sequence to be the same, on the tones which the SIG field occupies, in each 2MHz sub-band—refer to 11n GF 40MHz HTLTF and HTSIG designs.
According to current 11ah spec framework
  2MHz SIG field occupies 52+4 tones, in {-28:28} of 2MHz band—refer to [1].
  LTF sequences of 2/4/8/16MHz are the same as the 20/40/80/160 MHz VHTLTF sequences in 11ac.
STF
LTF1
SIG
DATA
LTF2
…
LTF_NLTF
QBPSK
Example: 4MHz, SU format
SIG

## Slide 6: Issues with Current 2MHz SIG (1)
4MHz/8MHz/16MHz transmissions have 5 and 6 guard tones at edges—same as in LTF sequences.
  Occupied tones: 4MHz: {-58:58}; 8MHz {-122:122}.
When a 2MHz SIG sent on 56 non-zero tones, is repeated in 4MHz/8MHz, the SIG field for those BWs will be left with only 3 and 4 guard tones
  Occupies 2 extra guard tones at each edge, and there is no LTF sent in these extra tones!
Same issue in MU packet “Omni-portion”
Field | Tone Mapping (2MHz) | Tone Mapping (4MHz)
LTF, DATA |  | 
SIG |  | 
-60
-4
4
60
-28
-1
1
28
-58
-2
2
58
A
-28
-1
1
28
A
A
B
B
B

## Slide 7: Issues with Current 2MHz SIG (1)
Reminder: In 11ac, the 40/80 MHz the VHT-LTF sequences are not repetitions of the 20MHz VHT-LTF
  No common 56 tones sequence exists in each 20MHz sub-band
  The only thing that repeats itself in the 40/80MHz, is a 52 tone sequence (26 tones each of LTF left and LTFright)
Consequently, 11ah LTF sequences in 4/8MHz do NOT have 56 tones which repeat in each 20MHz sub-band
If the SIG is sent on 56 tones in each 2MHz sub-band, receiver cannot demodulate SIG field as it does not know the LTF sequence
11ac 20MHz:
LSIG/VHTSIGA Tones
11ac 40MHz:
LSIG/VHTSIGA Tones
LSIG/VHTSIGA Tones
11ac 80MHz:
LSIG/VHTSIGA Tones
LSIG/VHTSIGA Tones
LSIG/VHTSIGA Tones
LSIG/VHTSIGA Tones

## Slide 8: Solution: Reduce 2MHz SIG to 48+4 Tones
The easiest solution is to send the 2MHz SIG field within tones {-26: 26} as in 11n/11ac.
SIG field modulation flow becomes the same as 11n/11ac HTSIG/VHTSIGA
  48 tone interleaver, instead of 52 tones
SIG field reduces to 48 bits—reduce number of PAID field to 9 bits, which is the same as 11ac PAID
 | SU | MU
Length / Duration | 9 | 9
MCS | 4 | 
BW | 2 | 2
Aggregation | 1 | 
STBC | 1 | 1
Coding | 2 | 5
SGI | 1 | 1
GID |  | 6
Nsts | 2 | 8
PAID | 12 9 | 
Reserved | 8 7 | 10 6
CRC | 4 | 4
Tail | 6 | 6
Total | 52 48 | 52 48

## Slide 9: Side Note
Presentation 11/1483r2 [1] added into TGah spec framework the following sentence, which is incorrect and needs to be removed:
  “LTF signs in the tones of each 2MHz sub-band, when overlapping with the tones with a stand-alone 2MHz LTF, have the same values as the corresponding signs in 2MHz LTF.”

## Slide 10: References
[1] 11/1483 r2 “11ah preamble for 2MHz and beyond”.

## Slide 11: Motion-1
Move to make the following text change in section R.3.2.1.1.A of the spec framework?
  “SIG Field
    2 symbols, each modulated using Q-BPSK, same as in 11n green field preamble.
    52 48 data tones occupying tones {-26:26} within each 2MHz subband, and modulated using 11n/11ac MCS0.
      Note that 11n HTSIG uses 48 data tones...”

## Slide 12: Motion-2
Do you agree to make the following change in section R.3.2.1.1.E of the spec framework?
  ….
  i. PAID: 12 9 bits PAID to accommodate more clients than 11ac, not needed for MU.
 | SU | MU
Length / Duration | 9 | 9
MCS | 4 | 
BW | 2 | 2
Aggregation | 1 | 
STBC | 1 | 1
Coding | 2 | 5
SGI | 1 | 1
GID |  | 6
Nsts | 2 | 8
PAID | 12 9 | 
Reserved | 8 7 | 10 6
CRC | 4 | 4
Tail | 6 | 6
Total | 52 48 | 52 48

## Slide 13: Motion-3
Move to remove the following sub-bullet in R.3.2.1.1.D of the spec framework?
  “ ….
  b. LTF signs in the tones of each 2MHz subband, when overlapping with the tones with a stand-alone 2MHz LTF, have the same values as the corresponding signs in 2MHz LTF.
  ….”